## Slide 3
vital sign
collector
(per patient and type)
vital sign input device
send signal
MyMedicalData
store
MonitorMe Dashboard
(GUI)
displays
Signal DB
snapshot creator
patient
personel
doctor
sign analyzer
(per type but using all signals)
MonitorThem
Patient DB
MonitorMe App
Notification creator
Analyse rule builder
Analyse Data Dispatcher
Component View

## Slide 4
Vital Signal
Event Channels
(One Topic per Signal type)
vital signal input device
MyMedicalData
MonitorMe Dashboard
(GUI)
External Data APIs
patient
personel
doctor
Signal Analyzer
Patient DB
MonitorMe App
Notification Event Channel
Analyse Rule Builder
Signal DB
Patient Signal
Collector
(all Signals per patient)
Raw Signal Persister
Event Driven
Component View
Event producer
Event Channel/Queue
Event Consumer
Microservice
MonitorThem

## Slide 5
Roles & Responsibilities
1 | Vital Sign input device
 | Collects raw data:
1.1 | heart rate
1.2 | blood pressure
1.3 | oxygen levels
1.4 | blood sugar
1.5 | respiration rate
1.6 | ECG
1.7 | body temperature
1.8 | sleep (awake/sleep)
2 | Patient Signal Collector
2.1 | Collects raw data 1.1-1.8 per patient
2.2 | Process raw data per patient (1 record)
2.3 | 20 records available for 1 Nurse Station
2.4 | 20 Records available every < 1s
2.5 | Every Record on Screen every 5s
2.6 | 100 s (20 x 5s) time to show 20 Records
2.7 | Data recorded and Stored for 24hrs (history)
2.8 | Receive and Record 6.5 Data (Consolidated Data)
2.9 | Receive and Record 6.6 Data (APP Data)
3 | Signal Persister
3.1 | Collects and stores Vital Signals
4 | MonitorMe Dashboard
4.1 | Collects data from Patient Signal Collector
4.2 | 20 Records (20 patients data) and Store in Patient DB
4.3 | Display the data (Dashboard)
4.4 | filters by time and vital signal
4.5 | Through a GUI a user can access history data
5 | Snapshot Creator
5.1 | Enable to create Snapshot from Signal DB
5.2 | Access Consolidated Data from Signal DB
5.3 | Capable to upload Snapshot to MyMedical Data ( 10 )
5.4 | HTTPS API
6 | Signal Analyzer
 | Adjust Thresolds dependant on Patient A/S
 | Calculate A/S and VS threshold to patient record
6.1 | If Trend on Blood Presure drops -->Patient S
6.2 | (A/S) Blood Pressure Threshold calculated and SET
6.3 | if Patient S Alarms Adjusted.
6.4 | If Patient A Alarms Adjusted
6.5 | If Trend heart rate drops -->Patient S
6.6 | (A/S) Heart Rate Threshold calculated and SET
6.7 | if Patient S Alarms Adjusted.
6.8 | If Patient A Alarms Adjusted
6.9 | If Respiration Rate drops -->Patient S
6.1 | (A/S) Respiration Rate Threshold calculated and SET
6.11 | if Patient S Alarms Adjusted.
6.12 | If Patient A Alarms Adjusted
7 | Notification Event Channel
7.1 | Monitor thresholds per patient (per record)
7.2 | Analize and Triggers Alerts (Notifications) to users
7.3 | Manage users who should recieve Notifications
7.4 | Build and Manages notifications to be sent to APP
7.5 | Build Consolidate Data to be sent to MonitorMe Dashboard
7.6 | Sent data to APP
7.7 | Send data to MonitorMe dashboard ( 3 )
8 | Analyze Rule Builder
8.1 | Collects Data from Signal Analyzer ( 5 )
8.2 | Send data to MonitorMe ( 9 )

## Slide 6
Architecture Characteristics
The Solution design is based on an Event-Driven Architecture, as this provide:
Escalability.- The solution is deployed in premises but based on a private cloud and designed to be escalable (initially up to 500 patients), this is achieved by a combination of proprietary devices, software and cloud native technologies.
Security.- Based on premises all data is secure and governed by the required medical standards according to the regional area where it is deployed; exposed APIs externally to integrate with SaaS is through a single point of integration by using an API Gateway.
Reliability.- Services and DBs decomposition allows to have high availability in the solution end to end. It is expected that 8 of the vital signals are monitored separately per specific sensors and data collected independently, see component ( 3 )is de-coupled for this specific purposed.
Performance.-By priorizing Event Driven architecture for NFRs data collection (periodicity) per each of the 8 vital signals, see component 1, the aim is to allow the overall solution to adjust to the dimensioned capacity performance.
Elasticity.- The Design is dimensioned based on the core initial Requirements; the deployment of microservices (see roles & responsibilities) allow the solution to cope with traffic peaks driven by users (doctors, nurses and other medical staff).
Atomicity.- Due to requirements to manage and process critital information as vital signals, we proposed decoupling of services and DBs-Intent in order to enable atomicity per transaction . (see Use Cases).

## Slide 7
Use Case 03: alert

## Slide 8
Use Case 03: alert

## Slide 9
Use Case 03: alert

## Slide 10
Use Case 03: alert

## Slide 11
Use Case 01: collect signal

## Slide 12
Use Case 02: create snapshot

## Slide 13
Use Case 03: alert